## Slide 1
Title
PH-ATM
CIVIL AVIATION AUTHORITY OF THE PHILIPPINES
AIR NAVIGATION SERVICE
AISS System
Module 02
AISS Hardware Components
Objective:
          Identify the PHATM AISS Hardware Components Using the GSSDD, HCMD, SIF, and Solution Description Documents.

## Slide 2
Title
AISS System
Distribution of AISS System
Notes: PHATM DOC.VOL1.BOOK3.P74
GSSDD – Global System/Segment Design Document
AISS System is a computer system with hardware components distributed nationwide.
The Central Site is located here in Manila. The operational servers are installed at Manila ATMC while the failover servers at the Mactan ANF. Data from the operational servers are being replicated to the failover servers via the internet and vsat link.
Hosts (client and working positions) within the central site are connected via LAN while remote hosts are connected to the central site via WAN (microwave, vsat, internet).
As with other computer systems, the AISS Hardware implementation is composed of: (next slide)

## Slide 3
Title
AISS System
AISS Hardware Components
Servers
KVM Consoles & KVM Switches
Storage & Backup Devices
Network Appliance
Workstations
Display Devices
Printers & Plotters
Computer Peripherals
Notes: smartAIM Solution Description
Appendix A: AIS System - Hardware Item List
Reference to the documents:
• Attach_A_PH-ATM PK1_AISS_RFA_List_RevF.xsl
• P1ES-EI-14-002.pdf
Hardware Configuration Management Document

## Slide 4
Title
AISS System
Central Site – Manila ATMC
AISS Rack
Front View Rear View
Notes: PHATM DOC.VOL1.BOOK1 – Site Installation File (Manila ATM Centre)
AISS Rack is located at Communications Equipment Room – First Floor.
AISS Rack – 42 Unit
Major hardware components are being

## Slide 5
Title
AISS System
Central Site – Manila ATMC
AISS Rack
Cabinet:
Manufacturer:
Type:
Height:
Units:
Width:
Depth:
Frame Material:
Side covers:
Doors:
Housing color:
Fittings color:
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
AISS Rack is located at Communications Equipment Room – First Floor.
AISS Rack – 42 Unit

## Slide 6
Title
AISS System
Central Site – Manila ATMC
AISS Rack
Servers:
3 Operational Servers:
              HP ProLiant DL380p Gen8 SFF
              Node Names: (MAN-ESX-01, 02 & 03)
1 T&D Server:
              HP ProLiant DL380p Gen8 SFF
              Node Name: (MAN-ESX-04)
Notes: Equipment Name / Node Name

## Slide 7
Title
AISS System
Central Site – Manila ATMC
AISS Rack
Storage Devices:
1 SAN Storage
              HP MSA P2040 SFF SAN Storage
              (MAN-STO-01)
2 SAN Switches
              HP 8/8 (8)-Ports Enabled SAN Switch
              (MAN-SSW-01 & 02)
Notes: Which data are being stored?
8GB Fibre Channel SAN Switch

## Slide 8
Title
AISS System
Central Site – Manila ATMC
AISS Rack
Backup Devices:
1 Backup Server:
              HP ProLiant DL360p Gen8 SFF
              Node Name: (MAN-BCK-01)
1 Tape Library
              HP MSL2024 1 LTO-4 Ultrium 1840 FC TP Lib
              (MAN-TAP-01)
Notes: Which data are being backed up?
Verify Tape Library if Fibre Channel or SAS?

## Slide 9
Title
AISS System
Central Site – Manila ATMC
AISS Rack
KVM Console:
1 Rackmount KVM Console
              HP TFT7600 US G2, All-in-One Rack Konsole
              (MAN-CON-01)
KVM Switch:
1 Rackmount KVM Switch
              HP 0x2x8 KVM Switch
              (MAN-KVM-01)

## Slide 10
Title
AISS System
Central Site – Manila ATMC
AISS Rack
Network Appliance:
2 Cisco Switches
              Cisco Catalyst WS-C2960G-48TC-L Switch
              (MAN-SWI-01 & 02)
2 Cisco Firewalls
              Cisco ASA 5512X Security Plus Firewall
              (MAN-FWF-01 & 02)

## Slide 11
Title
AISS System
Central Site – Manila ATMC
WEB 01 Rack
Notes: PHATM DOC.VOL1.BOOK1 – Site Installation File (Manila ATM Centre)
WEB 01 Rack is located at Communications Equipment Room – First Floor.
MNWSLAN03SW – VPN Support

## Slide 12
Title
AISS System
Central Site – Manila ATMC
WEB 01 Rack
Network Appliance:
1 Cisco Switch for Support
              Cisco Catalyst 2960 24X
              (MNWSLAN03SW)
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
WEB 01 Rack is located at Communications Equipment Room – First Floor.
MNWSLAN03SW – VPN Support

## Slide 13
Title
AISS System
Central Site – Manila ATMC
WEB 02 Rack
Notes: PHATM DOC.VOL1.BOOK1 – Site Installation File (Manila ATM Centre)
WEB 02 Rack is located at Communications Equipment Room – First Floor.
ATMC Client Switch (except TEC Client) - MNAILAN1ASW ( AISS A) & MNAILAN1BSW (AISS B)
              DMZ - MNWSLAN2ASW & MNWSLAN2BSW

## Slide 14
Title
AISS System
Central Site – Manila ATMC
WEB 02 Rack
Network Appliance:
2 Cisco Switches for Central Site Clients
              Cisco Catalyst 3750G 48X 10/100/1000 /4SFP Standard Multilayer Image
              (MNAILAN1ASW & MNAILAN1BSW)
2 Cisco Switches for DMZ
              Cisco Catalyst 2960 24X
              (MNWSLAN2ASW & MNWSLAN2BSW)
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
WEB 02 Rack is located at Communications Equipment Room – First Floor.
ATMC Client Switch (except TEC Client) - MNAILAN1ASW ( AISS A) & MNAILAN1BSW (AISS B)
              DMZ - MNWSLAN2ASW & MNWSLAN2BSW
The small form-factor pluggable (SFP) is a compact, hot-pluggable
optical module transceiver used for both telecommunication and data
communications applications. The form factor and electrical interface are
specified by a multi-source agreement (MSA) under the auspices of the
Small Form Factor Committee.[1] It is a popular industry format jointly
developed and supported by many network component vendors.

## Slide 15
Title
AISS System
Central Site – Manila ATMC
BackBone-A Rack
Notes: PHATM DOC.VOL1.BOOK1 – Site Installation File (Manila ATM Centre)
BackBone Rack is located at Communications Equipment Room – First Floor.
              MNBBNET1ART (Rack A)

## Slide 16
Title
AISS System
Central Site – Manila ATMC
BackBone-B Rack
Notes: PHATM DOC.VOL1.BOOK1 – Site Installation File (Manila ATM Centre)
BackBone Rack is located at Communications Equipment Room – First Floor.
              MNBBNET1BRT (Rack B)

## Slide 17
Title
AISS System
Central Site – Manila ATMC
BackBone Rack
Network Appliance:
2 Cisco Routers
              Cisco Catalyst 2821 16X
              (MNBBNET1ART & MNBBNET1BRT)
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
BackBone Rack is located at Communications Equipment Room – First Floor.
Backbone Routers
              MNBBNET1ART (Rack A)
              MNBBNET1BRT (Rack B)

## Slide 18
Title
AISS System
Central Site – Manila ATMC
Communication Equipment Room
AIS Technical Workstation:
1 AISS LAN Control Workstation
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
              Node Name: (MAN-TEC-01)
AIS Printer:
            1 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
MAN-TEC-01 (CWP 72 / AIS Control) & MAN-PRN-13 – Located at Communications Equipment Room, First Floor

## Slide 19
Title
AISS System
Central Site – Manila ATMC
AIS Room
AIS Workstations:
4 AIS Workstations w/ AMHS UA
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
              Node Names: (MAN-WKS-04, 05, 14 & 15)
2 Map/Charting Workstations
              HP Z230 Tower Workstation
              HP Z30I 30-Inch IPS Monitor
              HP Z22I 21.5-Inch IPS Monitor
              GTCO CalComp A1 Tablet Digitizer, Drawing Board VI – 2436
              Node Names: (MAN-WKS-12 & 13)
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
CWP 51 / AIS 01 / MAN-WKS-14
CWP 54 / AIS 02 / MAN-WKS-04
CWP 61 / AIS 03 / MAN-WKS-05
CWP 60 / AIS 04 / MAN-WKS-15
CWP 52 / MAP-01 / MAN-WKS-12
CWP 56 / MAP-02 / MAN-WKS-13

## Slide 20
Title
AISS System
Central Site – Manila ATMC
AIS Room
AIS Workstations:
2 eAIP Workstations
              HP Z230 Tower Workstation
              HP Z30I 30-Inch IPS Monitor
              HP Z22I 21.5-Inch IPS Monitor
              Node Names: (MAN-WKS-10 & 11)
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
CWP 53 / AIP-01 / MAN-WKS-10
CWP 57 / AIP-02 / MAN-WKS-11

## Slide 21
Title
AISS System
Central Site – Manila ATMC
AIS Room
AIS Printers:
            3 HP OfficeJet7110 Wide Format ePrinter
            2 Brother MFC-J5910DW MFP A3 Color Ink Print Scan
AIS Plotters:
              2 HP DesignJet T2500 e-Multifunction Printer
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
HP OfficeJet7110 Wide Format ePrinter
CWP 51 MAP-01 MAN-PRN-14
CWP 54 AIS-03 MAN-PRN-04
CWP 60 AIS-04 MAN-PRN-14
Brother MFC-J5910DW MFP A3 Color Ink Print Scan
CWP 52 MAP-01?AIP01 MAN-PRN-11
CWP 56 MAP-02 MAN-PRN-12
  HP DesignJet T2500 e-Multifunction Printer
AIS Plotter 1 MAP-1 MAN-PLT-01
AIS Plotter 2 MAP-2 MAN-PLT-02

## Slide 22: Manila ATMC AIS Room Workstations (Other Subsystems)
AISS System
1 CADAS User Agent Position Workstation (CADAS-UA 2)
  HP Comp ProDesk 600 G1 SSF - Intel i5 4570 3.2GHz
  HP Elite Display E231
2 GSMS Workstations (RAIM-MO-001 & 002)
  NEC Express5800/53La – Intel Pentium Processor G6950 (2.80GHz)
  24 inch Widescreen LCD Monitor
1 MDPS Supervision Workstation (MDPS-01)
  HP Z400 Workstation - Intel 3550 3.0Ghz
  HP 24" Compaq Monitor
1 ADEW Workstation (MNAWWKS01WI)
  HP Z400 Workstation - Intel Xeon 3520 2.66 GHz
  Barco MDRC 2224 24" Monitor
  Gorgy LEDI 2/S Console Clock NTP 10/100BaseT
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
AMHS Subsystem
CWP 55 / AIDA-Ph-II Manila CADAS-UA 2 / CADAS-UA 2
GSMS Subsystem
CWP 58 / RAIM-MO-001 / --
CWP 59 / RAIM-MO-002 / --
MDPS Subsytem
CWP 62 / MDPS-01 / --
ADEW Subsystem
CWP 63 / ADEW-1 / MNAWWKS01WI (ODS7)

## Slide 23: Manila ATMC AIS Room Printers and Plotters (Other Subsystems)
AISS System
Printers
  1 HP LaserJet Pro 400 M401D 33ppm S7W, Duplex 1200dpi
  1 HP Color LaserJet CP5525dn Printer
  1 HP CP5525dn A3 LaserJet Colour Printer
Plotters
  1 HP DesignJet Z6200 A1 Plotter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
AMHS Subsystem
HP LaserJet Pro 400 M401D 33ppm S7W, Duplex 1200dpi
GSMS Subsystem
HP Color LaserJet CP5525dn Printer
MDPS Subsytem
HP CP5525dn A3 LaserJet Colour Printer
ADEW Subsystem
HP DesignJet Z6200 A1 Plotter

## Slide 24
Title
AISS System
Central Site – Manila ATMC
RCC Room
AIS Workstation:
1 AIS Workstation
              HP Z230 Tower Workstation
              HP Z30I 30-Inch IPS Monitor
              HP Z22I 21.5-Inch IPS Monitor
              Node Name: (MAN-WKS-07)
AIS Printer:
            1 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
CWP 99 AIS-1 MAN-WKS-07
CWP 99 AIS-1 MAN-PRN-08

## Slide 25
Title
AISS System
Central Site – Manila ATMC
FIS Room
AIS Workstations:
1 AMS Monitoring Workstation
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
              Node Name: (MAN-WKS-09)
1 FSS Monitoring Workstation
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
              Node Name: (MAN-WKS-08)
AIS Printers:
            2 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
AMS
CWP 128 AIS/AMHS MAN-WKS-09
CWP 128 AIS/AMHS MAN-PRN-10
FSS
CWP 125 AIS/AMHS MAN-WKS-08
CWP 125 AIS/AMHS MAN-PRN-09

## Slide 26
Title
AISS System
Central Site – Manila ATMC
ATM Operations Room
AIS Workstations:
3 AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
              Node Names: (MAN-WKS-01, 02 & 03)
AIS Printers:
            3 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
CWP-35 AIS/AMHS-1 MAN-WKS-02
CWP-35 AIS/AMHS-1 MAN-PRN-02
CWP-39 AIS/AMHS-2 MAN-WKS-03
CWP-39 AIS/AMHS-2 MAN-PRN-03
CWP-47 AIS-1 MAN-WKS-01
CWP-47 AIS-1 MAN-PRN-01

## Slide 27
Title
AISS System
Central Site – Manila ATMC
Briefing Room
AIS Workstation:
1 AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
              Node Name: (MAN-WKS-06)
AIS Printer:
            1 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)
CWP-69 AIS MAN-WKS-06
CWP-70 AIS MAN-PRN-07

## Slide 28
Title
AISS System
Central Site – CAAP HQ
ANS Central Office
AIS Workstation:
1 AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
AIS Printer:
            1 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)

## Slide 29
Title
AISS System
Central Site – CAAP HQ
Operations Center (OPCEN)
AIS Workstation:
1 AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
AIS Printer:
            1 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)

## Slide 30
Title
AISS System
Central Site – CAAP HQ
ATC Central Office
AIS Workstation:
1 AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
AIS Printer:
            1 HP OfficeJet7110 Wide Format ePrinter
Notes: PHATM DOC.VOL1.BOOK2 – Hardware Configuration Management Document (Manila ATM Centre)

## Slide 31
Title
AISS System
Remote Sites – via Microwave Link
NAIA ANF
AIS Workstations:
AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
AIS Printer:
            HP OfficeJet7110 Wide Format ePrinter
Notes: NAIA Tower
Verify if 2 workstations. NAIA Tower and (NAIA FSS instead of Tagaytay ANF).
Verify if Tagaytay ANF workstation exists.

## Slide 32
Title
AISS System
Remote Sites – via Microwave Link
Tagaytay ANF
AIS Workstations:
AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
AIS Printer:
            HP OfficeJet7110 Wide Format ePrinter
Notes: Inconsistent
HCMD – Tagaytay
SIF Port – NAIA
SOD – NAIA FSS
Verify if Tagaytay ANF workstation exists.

## Slide 33
Title
AISS System
Remote Sites – via VSAT
Nationwide Remote Sites
AIS Workstations:
AIS/AMHS Workstations
              HP Z230 Tower Workstation
              HP Z22I 21.5-Inch IPS Monitor
AIS Printer:
            HP OfficeJet7110 Wide Format ePrinter

## Slide 34
Title
AISS System
Failover Site – Mactan ANF
Refer to Mactan ANF Documents:
      Hardware Configuration Management Document
      Global System/Segment Document
      Site Installation File
Notes: Proceed on ATMC Facility Tour.

## Slide 35
Title
AISS System
Hardware Interconnections
Refer to PHATM Documents:
      Hardware Configuration Management Document
      Global System/Segment Document
      Site Installation File
      SmartAIM Solution Description
    Use updated copies of such documents.
Notes: AISS to ATMC Back Bone
AISS to DMZ
AISS to Support
Port Allocations
Inconsistencies (AISS)
CPRTLAN01SW (BackboneDiagram) vs CPAILAN01SW01 (MNAILAN1ASW PortAllocation)
CPRTLAN01SW has no PortAllocation Diagram, secure updated copy..
Update MNAILAN(1A & 1B)SW PortAllocation
Verify if AIS workstations and working positions are connected to MNAILAN1ASW or CAAP Switch?
Verify location of CAAP Switch?

## Slide 36
Facility Tour…

## Slide 37
Title
AISS System
Facility Tour – AISS System
Manila ATMC Building
        Communications Equipment Room
        AIS Room
        RCC Room
        FIS Room
        Operations Room
        Briefing Room
Back To AISS Rack
Notes:         Need keys for abovementioned rooms.
        Need keys for AIS Rack, Backbone Rack A&B, and Web02 Rack.

## Slide 38
Title
AISS System
Communications Equipment Room
Back To AISS Rack
Notes: AISS LAN Control Workstation
CWP 72 / AIS Control / MAN-TEC-01
MAN-PRN-13
WEB 02 Rack
MNAILAN1ASW (AISS A)
MNAILAN1BSW (AISS B)
AISS Rack

## Slide 39
Title
AISS System
Communications Equipment Room
Back To AISS Rack
Notes: Request for access information: e.g. Username/Password for OS and applications.
MAN-TEC-01 (CWP 72 / AIS Control) & MAN-PRN-13 – AKA AISS LAN Control Workstation
AISS Rack
WEB 02 Rack - MNAILAN1ASW ( AISS A) & MNAILAN1BSW (AISS B)

## Slide 40
Title
AISS System
AIS Room
Back To AISS Rack
Notes: 4 AIS Workstations
CWP 51 / AIS 01 / MAN-WKS-14
CWP 54 / AIS 02 / MAN-WKS-04
CWP 61 / AIS 03 / MAN-WKS-05
CWP 60 / AIS 04 / MAN-WKS-15
2 eAIP Workstations
CWP 53 / AIP-01 / MAN-WKS-10
CWP 57 / AIP-02 / MAN-WKS-11
2 Map/Charting Workstations
CWP 52 / MAP-01 / MAN-WKS-12
CWP 56 / MAP-02 / MAN-WKS-13
3 HP OfficeJet 7110 Printers
CWP 51 MAP-01 MAN-PRN-14
CWP 54 AIS-03 MAN-PRN-04
CWP 60 AIS-04 MAN-PRN-14
2 Brother MFC-J5910DW Printers
CWP 52 MAP-01?AIP01 MAN-PRN-11
CWP 56 MAP-02 MAN-PRN-12
2 HP DesignJet T2500 Plotters
AIS Plotter 1 MAP-1 MAN-PLT-01
AIS Plotter 2 MAP-2 MAN-PLT-02

## Slide 41
Title
AISS System
AIS Room
Back To AISS Rack
Notes: Right Wing

## Slide 42
Title
AISS System
AIS Room
Back To AISS Rack
Notes: Center

## Slide 43
Title
AISS System
AIS Room
Back To AISS Rack
Notes: Left Wing

## Slide 44
Title
AISS System
RCC Room
Back To AISS Rack
Notes: Verify if AIS Working Position or AIS/AMHS Workstation.
CWP 99 AIS-1 MAN-WKS-07
CWP 99 AIS-1 MAN-PRN-08

## Slide 45
Title
AISS System
RCC Room
Back To AISS Rack

## Slide 46
Title
AISS System
FIS Room
Back To AISS Rack
Notes: AMS
CWP 128 AIS/AMHS MAN-WKS-09
CWP 128 AIS/AMHS MAN-PRN-10
FSS
CWP 125 AIS/AMHS MAN-WKS-08
CWP 125 AIS/AMHS MAN-PRN-09

## Slide 47
Title
AISS System
FIS Room
Back To AISS Rack
Notes: AMS
CWP 128 AIS/AMHS MAN-WKS-09
CWP 128 AIS/AMHS MAN-PRN-10
FSS
CWP 125 AIS/AMHS MAN-WKS-08
CWP 125 AIS/AMHS MAN-PRN-09

## Slide 48
Title
AISS System
ATM Operations Room
Back To AISS Rack
Notes: CWP-35 AIS/AMHS-1 MAN-WKS-02
CWP-35 AIS/AMHS-1 MAN-PRN-02
CWP-39 AIS/AMHS-2 MAN-WKS-03
CWP-39 AIS/AMHS-2 MAN-PRN-03
Verify Equipment/Node Name
CWP-47 AIS-1 MAN-WKS-01
CWP-47 AIS-1 MAN-PRN-01

## Slide 49
Title
AISS System
ATM Operations Room
Back To AISS Rack
Notes: CWP-35 AIS/AMHS-1 MAN-WKS-02
CWP-35 AIS/AMHS-1 MAN-PRN-02
CWP-39 AIS/AMHS-2 MAN-WKS-03
CWP-39 AIS/AMHS-2 MAN-PRN-03
Verify Equipment/Node Name
CWP-47 AIS-1 MAN-WKS-01
CWP-47 AIS-1 MAN-PRN-01

## Slide 50
Title
AISS System
ATM Operations Room
Back To AISS Rack
Notes: CWP-35 AIS/AMHS-1 MAN-WKS-02
CWP-35 AIS/AMHS-1 MAN-PRN-02
CWP-39 AIS/AMHS-2 MAN-WKS-03
CWP-39 AIS/AMHS-2 MAN-PRN-03
Verify Equipment/Node Name
CWP-47 AIS-1 MAN-WKS-01
CWP-47 AIS-1 MAN-PRN-01

## Slide 51
Title
AISS System
Briefing Room
Back To AISS Rack
Notes: CWP-69 AIS MAN-WKS-06
CWP-70 AIS MAN-PRN-07

## Slide 52
Title
AISS System
Briefing Room
Back To AISS Rack
Notes: CWP-69 AIS MAN-WKS-06
CWP-70 AIS MAN-PRN-07

## Slide 54
Title
Preventive Maintenance
        Perform periodic system status check through local and central monitoring systems (Zabbix and WUG-CTMS) and then take appropriate actions if necessary.
        Perform the recommended practices based on the AISS Maintenance Manual and Hardware Documentations.
        Within Warranty Contract:
          Request guidance from Thales Engineers if necessary.
AISS System
Notes: Cleaning
Handling
Storage
Spare Parts Periodic Check
e.g. Clarifications re procedures.

## Slide 55
Title
Corrective Maintenance
        Within Warranty Contract:
          Perform corrective actions as stipulated in the warranty contract.
        Beyond Warranty Contract:
          Perform the recommended corrective actions based on the AISS Maintenance Manual and other relevant hardware documents available.
AISS System
Notes: PCRs

## Slide 56
Title
AISS System
SUMMARY
In this module, the AISS Hardware Components and their corresponding locations were identified:
Servers
Consoles & KVMs
Storage & Backup Devices
Network Appliance
Workstations
Display Devices
Printers & Plotters
Computer Peripherals

## Slide 57
Title
SUMMARY
        Operational & T&D Servers:
        HP ProLiant DL380p Gen8 SFF
        Console:
        HP TFT7600 US G2, All-in-One Rack Konsole
        KVM:
        HP 0x2x8 KVM Server Console Switch
AISS System

## Slide 58
Title
SUMMARY
        Storage Devices:
        HP MSA P2040 SFF SAN Controller
        HP 8/8 (8)-Ports Enabled SAN Switch
        Backup Devices:
        HP ProLiant DL360p Gen8 SFF
        HP MSL2024 Tape Library & LTO Ultrium Tape
AISS System

## Slide 59
Title
SUMMARY
        Workstations:
        HP Z230 Tower Workstations
        Display:
        HP Z30I 30-Inch IPS Monitor
        HP Z22I 21.5-Inch IPS Monitor
        Network Appliance:
        Cisco ASA 5512X Security Plus Firewall
        Cisco Catalyst 3750G 48X 10/100/1000 /4SFP
        Cisco Catalyst WS-C2960G-48TC-L Switch
        Cisco Catalyst 2821 16x Router
AISS System

## Slide 60
Title
SUMMARY
        Printers:
        HP OfficeJet7110 Wide Format ePrinter
        Brother MFC-J5910DW MFP A3 Color Ink Print Scan
        Plotters:
        HP DesignJet T2500 e-Multifunction Printer
        Peripherals:
        Mouse
        Keyboard
        GTCO CalComp A1 Tablet Digitizer, Drawing Board
        UPS
AISS System

## Slide 61
Title
End..

## Slide 63
Title
AISS System
HP ProLiant DL380p G8 SFF
Back To AISS Rack

## Slide 64
Title
AISS System
HP ProLiant DL380p G8 SFF
Back To AISS Rack

## Slide 65
Title
AISS System
HP ProLiant DL380p G8 SFF
Front panel LEDs and buttons
Back To AISS Rack
Notes: Front panel LEDs and buttons

## Slide 66
Title
AISS System
HP ProLiant DL380p G8 SFF
System Insight Display
Back To AISS Rack
Notes: HP ProLiant DL380p Gen8 System Insight Display

## Slide 67
Title
HP ProLiant DL380p G8 SFF
SAS (Serial Attached SCSI) Hard Disk
        Capacity :
        Speed : 10,000 rpm
        Random access time : 4 ms
        Transfer rate : 6 Gbps
        Interface : 6 Gb/s SAS (Serial Attached SCSI)
        Size : SFF, 2.5”, 17.78 x 11.76 cm (W x H)
        Hot-swappable
AISS System
Back To AISS Rack

## Slide 68
Title
HP ProLiant DL380p G8 SFF
SAS (Serial Attached SCSI) Hard Disk LEDs
AISS System
Back To AISS Rack
Notes:         Capacity :
        Speed : 10,000 rpm
        Random access time : 4 ms
        Transfer rate : 6 Gbps
        Interface : 6 Gb/s SAS (Serial Attached SCSI)
        Size : SFF, 2.5”, 17.78 x 11.76 cm (W x H)
        Hot-swappable

## Slide 69
Title
AISS System
HP ProLiant DL380p G8 SFF
Back To AISS Rack

## Slide 70
Title
AISS System
HP ProLiant DL380p G8 SFF
Back To AISS Rack

## Slide 71
Title
AISS System
HP ProLiant DL380p G8 SFF
Back To AISS Rack
Notes: Fibre Channel, or FC, is a high-speed network technology (commonly running at 1, 2, 4, 8, 16, 32, and 128 gigabit per
second rates) primarily used to connect computer data storage to servers. Fibre Channel is mainly used in storage
area networks (SAN) in commercial data centers. Fibre Channel networks form a switched fabric because they operate in
unison as one big switch. Fibre Channel typically runs on optical fiber cables within and between data centers.
FlexibleLOM ports (Shown: 4 ports 1Gb each /Optional: 2ports 10Gb each)

## Slide 72
Title
AISS System
HP ProLiant DL380p G8 SFF
Item | Specification
Processors (Dual) | Intel Xeon E5-2600 v2 series
Memory (installed) | 256 GB
Memory Slots | 24 DIMM slots: DDR3 Registered (RDIMM), Load Reduced (LRDIMM), or Unbuffered (UDIMM) memory
Chipset | Intel C600 Series Chipset Intel E5-2600 and E5-2600 v2 Processor Families
On System Management Chipset | HP iLO (Firmware: HP iLO 4) NOTE: For more information, visit: http://www.hp.com/go/ilo
Expansion Slots | PCIe 3.0 Slots 1, 2, 3-PCIe 2.0 top to bottom PCIe 3.0 Slots 4-6 top to bottom
Maximum Internal Storage | 30TB Hot Plug SFF SAS
Back To AISS Rack

## Slide 73
Back To AISS Rack

## Slide 74
Title
AISS System
HP 8/8 (8)-Ports Enabled SAN Switch
Back To AISS Rack
Notes: Check if 8-port or 24-port..
2 SAN Switches
HP 8/8 (8)-Ports Enabled SAN Switch
(MAN-SSW-01 & 02)

## Slide 75
Title
AISS System
HP 8/8 (8)-Ports Enabled SAN Switch
Back To AISS Rack
Notes: Check if 8-port or 24-port..
2 SAN Switches
HP 8/8 (8)-Ports Enabled SAN Switch
(MAN-SSW-01 & 02)

## Slide 76
Back To AISS Rack

## Slide 77
Title
AISS System
HP MSA P2040 SFF SAN Storage
Back To AISS Rack
Notes: All data and applications on the smartAIM servers and the servers themselves are stored on the SAN. The local disks of the physical servers are only used for the VMware operating system.
The connection to the storage is provided via fibre channel.
A storage area network (SAN)[1] is a network which provides access to consolidated, block level data storage. SANs are
primarily used to enhance storage devices, such as disk arrays, tape libraries, and optical jukeboxes, accessible to servers
so that the devices appear to the operating system as locally attached devices. A SAN typically has its own network of
storage devices that are generally not accessible through the local area network (LAN) by other devices. The cost and
complexity of SANs dropped in the early 2000s to levels allowing wider adoption across both enterprise and small to
medium-sized business environments.
A SAN does not provide file abstraction, only block-level operations. However, file systems built on top of SANs do
provide file-level access, and are known as shared-disk file system

## Slide 78
Title
AISS System
HP MSA P2040 SFF SAN Storage
Back To AISS Rack
Notes: All data and applications on the smartAIM servers and the servers themselves are stored on the SAN. The local disks of the physical servers are only used for the VMware operating system.
The connection to the storage is provided via fibre channel.

## Slide 79
Title
AISS System
HP MSA P2040 SFF SAN Storage
Back To AISS Rack

## Slide 80
Title
AISS System
HP MSA P2040 SFF SAN Storage
Back To AISS Rack
Notes: All data and applications on the smartAIM servers and the servers themselves are stored on the SAN. The local disks of the physical servers are only used for the VMware operating system.
The connection to the storage is provided via fibre channel.

## Slide 81
Back To AISS Rack

## Slide 82
Title
AISS System
HP ProLiant DL360p G8 SFF
Back To AISS Rack
Notes: A backup refers to the copying and archiving of computer data so it may be used to restore the original.
HP Data Protector – Backup software/tool used.
Full Backup - A repository of this type contains complete system images from one or more specific points in time.
Incremental Backup - An incremental style repository aims to make it more feasible to store backups from more points in time by organizing the data into increments of change between points in time.
Differential Backup - Each differential backup saves the data that has changed since the last full backup.

## Slide 83
Title
AISS System
HP ProLiant DL360p G8 SFF
Back To AISS Rack
Notes: A backup refers to the copying and archiving of computer data so it may be used to restore the original.
HP Data Protector – Backup software/tool used.
Full Backup - A repository of this type contains complete system images from one or more specific points in time.
Incremental Backup - An incremental style repository aims to make it more feasible to store backups from more points in time by organizing the data into increments of change between points in time.
Differential Backup - Each differential backup saves the data that has changed since the last full backup.

## Slide 84
Title
AISS System
HP ProLiant DL360p G8 SFF
Back To AISS Rack
Notes: A backup refers to the copying and archiving of computer data so it may be used to restore the original.
HP Data Protector – Backup software/tool used.
Full Backup - A repository of this type contains complete system images from one or more specific points in time.
Incremental Backup - An incremental style repository aims to make it more feasible to store backups from more points in time by organizing the data into increments of change between points in time.
Differential Backup - Each differential backup saves the data that has changed since the last full backup.
In computing, Serial Attached SCSI (SAS) is a point-to-point serial protocol that
moves data to and from computer-storage devices such as hard drives and tape drives.
SAS replaces the older Parallel SCSI (Parallel Small Computer System Interface,
usually pronounced "scuzzy" or "sexy"[2]) bus technology that first appeared in the
mid-1980s.
SAS-1: 3 Gbit/s (2005)
SAS-2: 6 Gbit/s (2009)
SAS-3: 12 Gbit/s (2013)
SAS-4: 24 Gbit/s (2017)

## Slide 85
Back To AISS Rack

## Slide 86
Title
AISS System
HP MSL 2024 – Tape Library
Back To AISS Rack

## Slide 87
Title
AISS System
HP MSL 2024 – Tape Library
Back To AISS Rack
Notes: Verify if Fibre Channel or SAS..

## Slide 88
Title
AISS System
HP LTO-4 Ultrium Tape
Back To AISS Rack

## Slide 89
Back To AISS Rack

## Slide 90
Title
AISS System
HP TFT7600 US G2 KVM Console
Back To AISS Rack
Notes: (a console represents one keyboard, video monitor, and mouse (KVM) attached to a server)
Designed for rack mount use, the HP TFT7600 US G2 KVM Console is ideal for datacenters, corporate computer rooms and even SMB installations where local access to servers is needed at the rack.
Designed to work with a variety of KVM Switches.

## Slide 91
Title
AISS System
HP TFT7600 US G2 KVM Console
Back To AISS Rack

## Slide 92
Title
AISS System
HP TFT7600 US G2 KVM Console
Back To AISS Rack
Notes: OSD – On-screen Display
The OSD buttons are used to operate the HP TFT7600 KVM Console OSD menus.
The OSD menu provides access to display settings and functions, enabling the user to customize the HP TFT7600 KVM Console display settings. (Brightness, Contrast, Image Control – Horizontal and Vertical, Language, Factory Settings, etc..)

## Slide 93
Title
AISS System
HP TFT7600 US G2 KVM Console
Back To AISS Rack

## Slide 94
Title
AISS System
HP TFT7600 US G2 KVM Console
Back To AISS Rack

## Slide 95
Title
AISS System
HP TFT7600 US G2 KVM Console
Back To AISS Rack

## Slide 96
Title
AISS System
HP TFT7600 US G2 KVM Console
12Vdc
Back To AISS Rack
Notes: Use either the PS/2 cables or USB keyboard/mouse cable when connecting the unit to a device. Do not use both.

## Slide 97
Title
AISS System
HP TFT7600 US G2 KVM Console
Item | Specification
Display Size | 43.9cm (17.3 inch)
Display Type | Flat panel, color-active matrix TFT LCD
Maximum Weight (unpacked) | 4.5 Kg (10 lb)
Resolution | 640 x 480 (VGA) through 1280 x 1024 (SXGA), 1440 x 900 (WXGA+)(recommended), and 1600 x 900 (WXGA+)
Monitor Input | Standard VGA connector
Connectivity | PS2 and USB
Pointing Device | Three-button touchpad with scroll bar
Power Supply | 12 Vdc/36 W
Rack Space | 1U
Back To AISS Rack
Notes: 1U = 1.75 inches or 44.45 cm

## Slide 98
Back To AISS Rack

## Slide 99
Title
AISS System
HP 0x2x8 KVM Switch
Back To AISS Rack
Notes: HP Server Console Switches are key components for rack mount implementations (a console represents one keyboard, video monitor, and mouse (KVM) attached to a server). The family of HP Server Console Switches allows multiple servers in a rack to be accessed and managed by one keyboard, monitor, and mouse. By using a console switch, as many as 256 computers running different operating systems can be managed. The 8-Port and 16-port Server Console Switches feature an On-Screen Display (OSD) interface, which has intuitive menus for accessing each attached computer or serial attached device. Equipment can be identified by a user-defined name or sequentially by number, enabling easy access.
HP Server Console Switches can be connected in a tiered fashion, to increase server access from eight servers to as many as 256 servers. Switching between computers is accomplished by typing a switching command at the keyboard, or by using the mouse to interact with the graphic interface of the selected computer via the OSD.
The HP Server Console Switch family of products is available in 8- and 16-Port versions. Both versions offers dual console support, allowing the flexibility of controlling switch configurations from more than one location, or by more than one user. Standard rack mounting of the HP Server Console Switches will take up 1U (1.75") of front panel rack space. However, the Switches can also be mounted in a "zero U" profile by mounting in the side rails of the rack, or behind the HP 1U Keyboard Drawer or the 1U TFT7600 Keyboard/monitor drawer.

## Slide 100
Title
AISS System
HP 0x2x8 KVM Switch
Back To AISS Rack

## Slide 101
Title
AISS System
HP 0x2x8 KVM Switch
Back To AISS Rack

## Slide 102
Title
AISS System
HP 0x2x8 KVM Switch
Back To AISS Rack
Notes: Target Applications and Markets
Network Administrators, System Administrators, Engineering Managers, Chief Information Officers, and Managers of Information Systems are all among the users who will see benefits from using the HP family of server console switches.
Easy access to multiple servers (any server with PS/2 or USB I/O connection port)
Multi-platform management from one console (Microsoft® Windows®, Novell, UNIX®, Linux etc)
Local control and management of servers HP Server Console
Features
On-Screen Display (OSD) – Displays system-related information on the console monitor, such as selected server name, status, power-up test data and configuration menus.
Programmable Scanning – An evaluation of system performance can be made by sequentially scanning any or all of the
computers in the system. Programmable scanning allows you to determine which computers to include as well as the duration of the connection.
Configuration NVRAM – NVRAM (non-volatile RAM) makes it easy to set configuration information using commands entered
from the keyboard. The NVRAM stores the resulting configuration until a user decision is made to change the information,
even if the unit loses power.
Password Protection – For protection against unauthorized users, the switch box provides a password option for security
purposes.
Switch Firmware Update – The application code of the switch can be quickly and easily updated via FLASH ROM. The port
communications settings are automatically configured to allow direct downloading from the connected computer.
Multiple Space Saving 0U Installation Methods –
Side Mount - Rails are provided for mounting the unit to the side of rack cabinets with side mounting capability.
Rear Rack Mount - HP Console Switches may be mounted behind a HP Integrated Keyboard and Drawer (257054-XXX), the TFT5600 or the TFT7600 rack mounted keyboard and monitor with slide rails provided with the switch.
Support for variety of server connections with Interface Adapters
PS/2
USB
VT 100 serial console support
BladeSystems support via front diagnostics connector
Multi-user console switches
The multi-user server console switch has two user ports for multiple user consoles, and multiple system ports as well (many-to-many). The multi-user console offer expanded flexibility, such as the following scenarios:
Simultaneous control of servers in both the data center and in other remote locations.
If there are multiple network administrators, a multiple console switch allows each of them to access all of the servers in their data center to diagnose problems, all from separate locations.

## Slide 103
Title
AISS System
HP 0x2x8 KVM Switch Connectors
Back To AISS Rack
Notes: May use USB instead of PS/2 interface.

## Slide 104
Title
AISS System
HP 0x2x8 KVM Switch Interconnection
Back To AISS Rack
Notes: May use USB instead of PS/2 interface.
The console switch system has at least one local port (based on the specific model) on the rear panel that enables the user to connect a keyboard, monitor, and mouse to the console switch for direct access.
Use the Main dialog box to view, configure, and control servers in the console switch system.
Accessing the Main dialog box
To access the Main dialog box, choose one of the following default key sequences.
• Print Scrn
• Ctrl + Ctrl
To configure the following additional key sequences, see Accessing the Menu dialog box (on page 24).
• Alt + Alt
• Shift + Shift
Soft switching to a previous server
Press the Print Scrn key, then press the Backspace key. This key combination toggles between the previous and current connection.

## Slide 105
Title
AISS System
HP 0x2x8 KVM Switch Interconnection
Back To AISS Rack
Notes: May use USB instead of PS/2 interface.

## Slide 106
Back To AISS Rack

## Slide 107
Title
AISS System
Cisco Catalyst WS-2960G-48TC-L Switch
Back To AISS Rack
Notes: 2 Cisco Switches
Cisco Catalyst WS-C2960G-48TC-L Switch
(MAN-SWI-01 & 02)

## Slide 108
Title
AISS System
Cisco Catalyst WS-2960G-48TC-L Switch
Back To AISS Rack
Notes: 2 Cisco Switches
Cisco Catalyst WS-C2960G-48TC-L Switch
(MAN-SWI-01 & 02)

## Slide 109
Back To AISS Rack

## Slide 110
Title
AISS System
Cisco ASA 5512X Security Plus Firewall
Back To AISS Rack
Notes: 2 Cisco Firewalls
Cisco ASA 5512X Security Plus Firewall
(MAN-FWF-01 & 02)

## Slide 111
Title
AISS System
Cisco ASA 5512X Security Plus Firewall
Back To AISS Rack
Notes: 2 Cisco Firewalls
Cisco ASA 5512X Security Plus Firewall
(MAN-FWF-01 & 02)

## Slide 112
Back To AISS Rack

## Slide 113
Title
AISS System
Cisco Catalyst 3750G 48X 10/100/1000/4FSP
Back To WEB02 Rack
Notes: Cisco Catalyst 3750G 48X 10/100/1000 /4SFP
The small form-factor pluggable (SFP) is a compact, hot-pluggable
optical module transceiver used for both telecommunication and data
communications applications. The form factor and electrical interface are
specified by a multi-source agreement (MSA) under the auspices of the
Small Form Factor Committee.[1] It is a popular industry format jointly
developed and supported by many network component vendors.
An SFP interface on networking hardware provides the device with a
modular interface that the user can easily adapt to various fiber optic and
copper networking standards. SFP transceivers exist supporting SONET,
Gigabit Ethernet, Fibre Channel, and other communications standards.
Due to its smaller size, the SFP has replaced the gigabit interface converter (GBIC) in most applications; the SFP is
sometimes referred to as a Mini-GBIC. In fact, no device with this name has ever been officially defined in the MSAs.

## Slide 114
Back To WEB02 Rack

## Slide 115
Title
AISS System
Cisco ASA 5510 Firewall
Back To AISS Rack
Installed at Mactan ANF only

## Slide 116
Title
AISS System
Cisco ASA 5510 Firewall
Back To AISS Rack
Installed at Mactan ANF only

## Slide 118
Title
AISS System
HP Z230 Tower Workstation
Back To AISS Rack

## Slide 119
Back To AISS Rack

## Slide 120
Title
AISS System
HP Z30i 30Inch IPS Monitor
Back To AISS Rack

## Slide 121
Title
AISS System
HP Z30i 30Inch IPS Monitor
Back To AISS Rack

## Slide 122
Back To AISS Rack

## Slide 123
Title
AISS System
HP Z22i 21.5Inch IPS Monitor
Back To AISS Rack

## Slide 124
Title
AISS System
HP Z22i 21.5Inch IPS Monitor
Back To AISS Rack

## Slide 125
Back To AISS Rack

## Slide 126
Title
AISS System
HP OfficeJet 7110 Wide Format ePrinter
Back To AISS Rack
Notes: HP OfficeJet7110 Wide Format ePrinter

## Slide 127
Back To AISS Rack

## Slide 128
Title
AISS System
Brother MFC-J5910DW MFP A3
Back To AISS Rack
Notes:         Brother MFC-J5910DW MFP A3 Color Ink Print Scan

## Slide 129
Back To AISS Rack

## Slide 130
Title
AISS System
HP DesignJet T2500 e-Multifunction Printer
Back To AISS Rack
Notes:         HP DesignJet T2500 e-Multifunction Printer

## Slide 131
Title
AISS System
HP DesignJet T2500 e-Multifunction Printer
Back To AISS Rack
Notes:         HP DesignJet T2500 e-Multifunction Printer

## Slide 132
Back To AISS Rack

## Slide 133
Title
AISS System
GTCO CalComp A1 Tablet Digitizer, Drawing Board VI
Back To AISS Rack
Notes:         GTCO CalComp A1 Tablet Digitizer, Drawing Board VI

## Slide 134
Title
AISS System
GTCO CalComp A1 Tablet Digitizer, Drawing Board VI
Back To AISS Rack
Notes:         GTCO CalComp A1 Tablet Digitizer, Drawing Board VI

## Slide 135
Title
AISS System
GTCO CalComp A1 Tablet Digitizer, Drawing Board VI
Back To AISS Rack
Notes:         GTCO CalComp A1 Tablet Digitizer, Drawing Board VI

## Slide 136
Title
AISS System
GTCO CalComp A1 Tablet Digitizer, Drawing Board VI
Back To AISS Rack
Notes:         GTCO CalComp A1 Tablet Digitizer, Drawing Board VI

## Slide 137
Title
AISS System
GTCO CalComp A1 Tablet Digitizer, Drawing Board VI
Back To AISS Rack
Notes:         GTCO CalComp A1 Tablet Digitizer, Drawing Board VI

## Slide 138
Back To AISS Rack